## Slide 1: Hop Hacking Hedy
atlas, cutaway and Q

## Slide 2: Authors
atlas
  Code monkey
  Magical debugging wizard
cutaway
  Radio-Fu
  Supreme dongle overlord
Q
  Hardware-Fu
  Creator of sexy slides

## Slide 3: Agenda
Prelude
  Hedy and her Patent
FHSSWTF
  Technical explanation
FHSS Usage and Analysis
  Case examples
    Problems revolving around FHSS
    Possible solutions
Project
  What we are developing
    Hardware: Devices Utilized, Debugging and Wiring Instructions
    Developing and Using the Code Base
  Practical Applications for decoding hopping patterns

## Slide 4: Prelude
Explanation of the Title
  What is a HEDY?
  Surprisingly not a lot of people understood the title
    That’s right, a focus group was held
  So I must explain!
Alternative Title
  “3 Dudes and a Dongle”
  Not sure we would have been accepted

## Slide 5: Prelude
This is a Hedy 

## Slide 6: Prelude
Hedy Lamarr
  Inventor
    Supremely nerdy
    nerd_chick++;
  Actress
    Less important here
    Sidenote: Military used her celebrity to sell War Bonds instead of her brains to join a panel of scientists during the war. 

## Slide 7: Prelude
Inventor of “secret communication system”
  Along with George Antheil
  Patent: 2,292,387
  Filed: June 10, 1941
Recognized by EFF in 1997 for her achievements
  Go EFF

## Slide 8: Prelude
Secret communication
  TX
    VFCO -> Modulator -> Amplifier
  RX
    Selector -> Amplifier -> Detector
      Noise reduction (filtering)
Ya, that’s a piano roll
  Used to change between 88 freqs.
  Ah, the days before digital
End Result
  Impressive for the days of Analog

## Slide 9: FHSSWTF
FHSS - Frequency Hopping Spread Spectrum
  Transmission method
    Carrier is rapidly switched in the frequency domain
    Multiple channels
      Depends upon bandwidth
        Bluetooth – 79 MHz
          @ 1MHz channel spacing – 79 channels
        Smart Meters – 26MHz
          @ 500 kHz channel spacing – 52 channels

## Slide 10: FHSSWTF
Pseudo-random sequence to choose frequencies
  Known by Transmitter and Receiver
    Multiple sync methods
  Stored algorithm within memory generates pattern
    Creates spread code sequence tables
    Possibly stored within a piano roll
      If you’re Hedy Lamarr

## Slide 11: FHSS USAGE
Who uses them?
  Military
    SINCGARS
      Single Channel Ground and Airborne Radio System
        Voice-and-Data
        25 kHz Channels
        30-88 MHz
          120-352 channels
          100 hops/second
            Very slow
            Expected to be replaced by an SDR solution
              Deployment issues

## Slide 12: FHSS ANALYSIS
SINCGARS
  Problem: 500,000 units purchased[1] Until the 2008 improvement programs, how many radios were relying on FHSS for security?
    How many still are?
  Solution: Upgrades provide voice-encryption, though backwards compatible with old radio hardware.
    Does security still exist if you’re supporting ancient hardware?
    SDR solution provides field-programmable devices
      Interesting!
      See: JTRS Project
    [1] – Reference: http://defensesystems.com/microsites/2010-peo-c3t/not-your-father-radios.aspx

## Slide 13: FHSS USAGE
Commercial
  Bluetooth
    Bandwidth:79 MHz
    Channel Spacing: 1 MHz
    Total Channels 79
      3200 clock cycles
        Hops every other
        1600 hops/second

## Slide 14: FHSS ANALYSIS
Bluetooth
  Problem: With commercially available hardware (USRPv2) you can generate hopping patterns for an entire technology within 24 hours and utilize this for future patterns.
  Solution: We can’t rely on FHSS as an implementation of a security model within our technology. We must do better.
    Encryption! Yes, please.

## Slide 15: FHSS Is not ENCRYPTION
“In FHSS, the frequencies to be used in the hopping sequence may be selected by the user. In the unlicensed band, any group of 26 frequencies or more (out of the 79 available) is legal. To “tune in”, a listener should know the number of frequencies selected in the system, the actual frequencies, the hopping sequence, as well as the dwell time! The FHSS modulation acts as a layer 1 encryption process. There could be no need for application level encryption!”
  Reference: “FHSS vs DSSS in Broadband Wireless Access and WLAN”
    Sorin M. Schwartz

## Slide 16: FHSS ANALYSIS
Why do we keep using it?
  Helps prevent overuse in unlicensed bands
    Especially with adaptive technology
Attack Vectors
  Must have the hopping pattern to jam or receive entire data stream
    Break the PRNG associated with the algorithm
      Obtain spread codes
    Analyze channel data in time domain fast enough to catch the hops until repeats start to occur
    Generate the entire pattern for all clock values
      Reference: Ossmann/Spill Shmoo 2009

## Slide 17: Solutions
Learn from our experience
  We have seen this issue in the Smart Grid industry
    Some 1st generation devices relied on FHSS as primary prevention of eavesdropping
    2nd and 3rd generation introduced encryption and signing of keys
  Do not rely on a single point of failure

## Slide 18: Project
Inspiration
  False assumptions that speed and pseudo random sequence creates a secure transmission
    Simply untrue with the powerful technology we have available
  Let’s build some devices that
    Can be configured for known ISM bands
    Automatically analyze channel spacing
    Can Decode FHSS Hopping Patterns
    Utilize a custom code-base with far-reaching capabilities to get people started
  That is the goal of our project …

## Slide 19: PROJECT
In 1942 Hedy Lamarr and George Antheil helped develop a system to assist in the prevention of jamming American radio-controlled torpedoes.
69 years later, it’s time to upgrade …

## Slide 20: H4RDW4RE
Cutaway’s Initial Interest
  Started out as bootstrap for hardware and firmware interaction
  Reading is one thing, but you don’t really know anything until you have destroyed something……that belongs to atlas
  Get to eat Sushi…at ShmooCon
  Get Tuna to buy me more drinks…at ShmooCon

## Slide 21: H4RDW4RE
Goodfet Graveyard
eZ430-Chronos Dongle

## Slide 22: H4RDW4RE
GoodME Project
  Cons
    Already being worked by atlas, Q, Travis, and Mike
    Pink might be pretty but some people just don’t get it
  Pros
    CC1110-based
    Great place to start
    Actively being worked

## Slide 23: H4RDW4RE
CC1111EMK868-915 Evaluation Module Kit
  CC1111-based
  All pins broken out
  Programmable via Goodfet
  Goodfet.cc interacts via Data Debug

## Slide 24: H4RDW4RE
Code Beginnings
  Hello World – Blinking LED
  Board data from TI’s IAR Demo
    Bloated and Complicated
  Reference documents for CC111*
  SmartRF Studio – provides radio data
  Specan code includes everything you need
    Watch your clocks and pins

## Slide 25: H4RDW4RE
Code Advances
  Prerequisites
    902 - 928 MHz Range
    Fast scanning
  Strip Specan Firmware Code
    Remove display (but compensate for delay)
    Shrink frequency range
  Leverage Goodfet
    Data Debug dumping
    Python scripts for displaying data
    Halting CPU – affects results

## Slide 26: H4RDW4RE
Resulting Firmware
  maxscan – spectrum analyzer
  hoptrans – create a carrier wave
    Number of channels is known
    Channel spacing is known
    Hop timing is known

## Slide 27: H4RDW4RE
Resulting Firmware (2)
  Minscan – detects channel hops
    Initializes frequencies
    Scans frequencies for minimum RSSI
    Monitors jumps in RSSI
    Stores detected spikes
    Data dump via Goodfet
    Data is analyzed offline

## Slide 28: H4RDW4RE
Issues
  Data Debug dump via Goodfet is slow
  Pausing CPU creates gaps in monitoring
  Memory on CC1111EMK is too small
  UART would work, but USB would be better
  CC1111EMK can do USB but must be managed via firmware

## Slide 29: H4RDW4RE
Lessons Learned
  Hardware is HARD
    When you start
    You WILL fail, drive on
  Hardware documentation is CONFUSING
    You get better with time
    The documentation DOES NOT
  Radios are complex
    Hardware radios ARE complicated
    SmartRF HELPS
    IM-ME code is an EXCELLENT example
  We CAN see good results in test data
    This IS step in a right direction

## Slide 30: C0DE
Overview
  CC1111
  Merging Code
  Screen Shots of Code Running
  GNU Plot
  Stages of Analysis
  Goals of Code
  Where we are Currently

## Slide 31: CC1111
USB-enabled version of TI’s most popular <1GHz radio/mcu
Same radio used in the majority of today’s Smart Meters
“easy” usb! Yeah right. YOU MUST READ “USB IN A NUTSHELL”
Separate cc1111usb project soon to be released
  GPL
  Hacker-written (good or bad?)
  Contained in one .c and one .h

## Slide 32: Merging Code
“Messing up code”
Still buggy, although somewhat less thrashing
USB code was *really* a mess when we started

## Slide 33: Screen shots of code running

## Slide 34: Intro to code
Python Client using libusb (requires admin access)
d.dump*() – grab large chunks of data from dongle
d.get*() – grab incidental settings
d.set*() – set incidental settings (threshold, channel info)
d.doFloorAndCeiling()
d.doChannelIdent()
d.doHopTracking()
d.interpret() – spits out formatted data, and plots
  GNUplot - Really fun way to wow people who don’t get gushy over green on black…

## Slide 35: Steps of analysis
Floor and Ceiling – mins and maxes
Channel threshold – how do we know when we’ve found a channel?
Channel Identification and Spacing – currently broke
Hopping pattern – this is the shizzle
  Predictive Analysis (future)
Sync Word – radios know when data is coming (future, easy)
Data Rate – duh, like a modem (future, limited possibilities, often documented)

## Slide 36: Goals of code
Dispell myths of FHSS security (obviously)
Weaponization and Automation
Network Sniffing
Network Participation
Reduce time for real security testing

## Slide 37: Where we’re at
USB-controlled radio – great platform to play
Calibration and Speed
Channel identification – broken but close
Hopping identification – some bugs in data storage and dumping
GNUplotting for hollywood enjoyment (hey hollywood)
Still need to analyze and coalesce final data better
Want to port it to the CC1110 of the IM-ME Dongle

## Slide 38: Acknowledgements
Travis Goodspeed
  Not only is he a master of the belt buckle but a supreme commander of all things Good and FET
  Check out the GoodFET project
    http://goodfet.sourceforge.net/
“Michael Ossmann Is My Hero”
  He has T-Shirts that say so …
  Creator of neighborly spectrum analysis software
    Developed at the last SHMOOCON!
    http://www.ossmann.com/
Bill Gates
Brett and Jemain, and Bagettes

## Slide 39: Project Information
Google Code Page
  http://code.google.com/p/hedyattack/
Member Information
  atlas
    atlas@r4780y.com
  Don C. Weber
    don@inguardians.com
  Andrew Righter
    andrew@inguardians.com

## Slide 40: Questions & Answers
if time_remaining != 0:
  answer_questions( );
else:
  print(“sorry!”);